## Slide 1: 3D Reconstruction of small Solar System bodies using rendered and compressed images
Thesis Presentation
By Gabriel J. Schwarzkopf
Supervisor: Jaan Praks; Advisor: Andris Slavinskis
LTU Examiner: Mikael Granvik

## Slide 2: Table of Contents
Motivation
Theory
Implementation
Results
Conclusion

## Slide 3: Motivation
Solar System formation
Remote vs In-situ
Small sat flyby
Confirmed missions
Synthetic image creation
Notes: Solar System formation
Limited Information from remote observations
In-situ more detailed information
Small sat flyby as compromise between number of targets and in-situ
Confirmed missions (Comet interceptor and Hera) and concepts (CASTAway and MANTIS and MAT)
Synthetic image creation because missing real images
Hapke model is empirical and has problems
SISPO provides solution

## Slide 4: Theory – Rendering
Notes: Rendering – how to get from 3D to 2D
- Solving rendering equation -> energy conservation

## Slide 5: Theory – Rendering
Transluscent
Object
Reflection
Refraction
Light
Pixel
Image
Solid object
Light source
Notes: Rendering
  Path tracing – reverse path tracing: ray originates in camera and terminates in light source (or infinity or too many bounces)
  bounces at object
  bouncing can be reflection, refraction, transmission
  Shaders - Programs, basically maths, that calculate transmission/reflection etc effects,

## Slide 6: Theory – Rendering
Transluscent
Object
Reflection
Refraction
Shadow
Pixel
Image
Solid object
Light source
Notes: Rendering
  Path tracing – reverse path tracing: ray originates in camera and terminates in light source (or infinity or too many bounces)
  bounces at object
  bouncing can be reflection, refraction, transmission
  Shaders - Programs, basically maths, that calculate transmission/reflection etc effects,

## Slide 7: Theory – Rendering
Notes: Rendering
  Composition: varying brightness levels -> we need to calibrate
Used from astronomy -> use reference star and calibrate
Not visible

## Slide 8: Theory – Reconstruction
Notes: Reconstruction, going from 2D to 3D
advances in computer vision
advances in computer power

## Slide 9: Theory – Computer Vision
Notes: Computer Vision
  SfM: multiple views of same object, like eyes but multiple
  Goal: find point cloud that describes object
  To get point cloud -> finding the same point from different images

## Slide 10: Theory – Computer Vision
Credits: R. Arnold (https://slideplayer.com/user/12404608/)
Notes: Computer Vision
  Finding features and matching
  Features are local meaningful parts of image, best case scaling invariant, rotation invariant, translation invariant
  Series of descriptors and detection combinations exist: SIFT

## Slide 11: Theory – Computer Vision
Notes: Computer Vision
  SfM – trace path of features in images
  Calculate epipolar lines and their intersection
  Incremental or global: incremental starts with pair and adds, global optimizes with all images at the same time
  Also estimating camera pose and distortion parameters
  Algorithms might not converge -> initial pair for incremental is important

## Slide 12: Implementation – Rendering
?
Notes: How is rendering done
Blender!
Using shader nodes,
  Procedural terrain generation -> we have smooth surface model
Basically different types of noise input is merged
Both images use same model, only three params changed

## Slide 13: Implementation – Rendering
Notes: Blender
  Composition
  Different brightnesses between images of series and calibration between stars and sssb
  Reference systems is UBV system, reference object is sun
  4 images are combined: sssbonly, stars, sssbconstdist, lightref (known brightness, therefore we know how to calibrate) -> composed
Stars too dark

## Slide 14: Implementation – Compression
Necessary in space
Small sats
Lossless and lossy formats
PNG/JP2000
Notes: Compression
  PNG and JP2000

## Slide 15: Implementation – Reconstruction
Point cloud densification
Mesh reconstruction
Mesh refinement
Mesh texturing
OpenMVS
Image listing
Feature computation
Feature matching
Sparse point cloud
Notes: SfM
  Complete SfM pipeline from images to textured model with OpenMVG/OpenMVS

## Slide 16: Results – Images
SISPO
Bennu
67P/C-G
Notes: Images
SISPO resembles asteroid not comet, though limited in some area
Missing gas and dust environment, jet

## Slide 17: Results – Images
Before
After
Notes: Calibration:
Difference in brightness between images
Absolute calibration gets rid of both

## Slide 18: Results – 3D Models
50 km – 10 km SSSB
100 km – 1 km SSSB
400 km – 1 km SSSB
100 km – 1 km SSSB
Notes: Different levels of detail:
when close, structure is wall-like flat
when moving away we have less detail so surface becomes smoother first
when moving even further away, model gets rougher
Problems that occured during reconstruction dev: Inside out-egg shell, holes in the surface
-changed parameters of reconstruction, most importantly, constant camera params (assumption calibration values known before launch)

## Slide 19: Results – Compression
PNG
JP2 1000
JP2 100
JP2 10
JP2 5
JP2 1
Notes: Compression intro artefacts
not much visible in png, 1000, 100, 10
minor changes visible in 5
major changes visible in 1

## Slide 20: Results – Compression
Notes: Difference images, L2-norm of difference of gray-scale between png and each image
In absolute terms, 10, 5 and 1 visible. Shape clearly visible in all, otherwise random noise
looking at relative scales, also 100 clearly and 1000 some visible. Also 100 is random noise

## Slide 21: Results – Compression
Notes: Same done for zommed in area:
in equal scale: 10 minor, 5 visible but mostly random, 1 clearly visible with features, other nothing
when using relative scale, also 100 visible. 100 random noise, 10 most prominent features, 5 a bit more features, 1 strong features all over

## Slide 22: Results – Compression
Notes: Clearly visible spreading
Increasing percentage of altered pixels

## Slide 23: Results – Compression
Notes: 1km scenario with different flyby distances
Most reconstructions work
Mostly, quality not worse but even better
When points high but vertices low -> outliers were filtred
400km too far for jp 1 does not work, other minorly
Why better? Because noise introduced, used as artefacts with sfm
Data size can be constant because of large black area which is easily compressed away

## Slide 24: Results – Compression
Notes: Similarly visible when looking at 10km sssb
All reconstructions work
Quality degreades with compression
Also higher results than with png. Despite 100km case, jp2 100 creates best results for the other 3 cases
Constantly decreasing, compression is more relevant to think about because of sssb taking full frame

## Slide 25: Conclusion
First step
Procedural terrain generation for asteroids
Compression introduces artefacts
Artefacts used by SfM
Gas and dust
Spacecraft motion & attitude
Imaging distortions
Notes: Sispo first step
Procedural creates good asteroid, comet needs gas and dust
Compression introduces artefacts
Artefacts are used by sfm to increase number of points
Future work
Gas and dust important
Spacecraft motion
Imaging distortions

## Slide 26: Conclusion

## Slide 27: Acknowledgements
School of Electrical Engineering – Aalto University
Supervisor: Jaan Praks
Advisor: Andris Slavinskis
LTU Examiner: Mikael Granvik
Special thanks: Mihkel Pajusalu

## Slide 28: Thank you for your attention!